## Slide 1: Real-Time Self-Testing Quantum Random Number Generator with Non-classical States
1 CQC2T, DQS, Australian National University
2LKB, Sorbonne Université, CNRS, ENS-PSL Research University, Collège de France
3 Department of Information Engineering, Università degli Studi di Padova
4 Istituto di Fotonica e Nanotecnologie, Università degli Studi di Padova
Currently at: *ECE, NUS Singapore ^Toshiba, CRL #Dipartimento di Fisica e Astronomia
Thibault Michel1,2, J.Y. Haw1*, D. G. Marangon3^, O. Thearle1, G. Vallone3,4 #, P. Villoresi3,4 , P. K. Lam1, S.M. Assad1
PhysRevApplied.12.034017
thibault.michel@anu.edu.au

## Slide 2: Outline
Introduction and motivation
Principle of the self-testing QRNG
Protocol and experimental implementation
Results
Outlook

## Slide 3
QKD requires secure and independent random numbers
Pseudo random numbers are intrinsically flawed
The “Quantum World” can provide intrinsic true randomness
  → Quantum Random Number Generators

## Slide 4
Trusted device QRNG
Device independent QRNG
ρ
SDI-QRNG
High bit rate (Gb/s) [1, 2]
Easy to implement
Need to trust the device
Device needs to be well characterized
Full security certified by non locality
Harder to implement
Slow bit rates (b-kb/s) [3-6]
[1] Symul et al. (2011). Applied Physics Letters, 98(23), 231103.
[2] Abellán et al. (2019). Optics express 22.2: 1645-1654
[3] Liu et al. (2018). Physical review letters, 120(1), 010503.
[4] Bierhorst et al. (2018). Nature, 556(7700), 223-226.
[5] Qcrypt 2020. Yanbao Zhang et al. Device-independent Randomness Expansion with Entangled Photons.
[6] Qcrypt 2020. Wen-Zhao Liu et al. Device-independent randomness expansion against quantum side information.
[7] Lunghi et al. (2015). Physical review letters, 114(15), 150501.
[8] Marangon et al. (2017). Physical review letters, 118(6), 060503.
Bit rate/ Ease of implementation
Security/ Paranoia level
[7, 8]

## Slide 5
Local
oscillator
Entropy source

## Slide 6
Local
oscillator
Entropy source
[1] Haw et al. (2015). Maximization of extractable randomness in a quantum random-number generator. Physical Review Applied, 3(5), 054004.

## Slide 7
Local
oscillator
Entropy source

## Slide 8
Entropic Uncertainty Relation (EUR):
Side Information
Eve
Alice
POVM
POVM
Raw
Numbers
Extraction
Secure
Numbers
Assumptions:
  Trusted measurement device (untrusted classical noise)
  I.I.D. and bounded source (untrusted)

## Slide 9
  Record dark and shot noise
  If P measurement: Collect data and estimate lower bound on conditional min-entropy with EUR and frequentist estimators
  If X measurement: Collect data, Hash it with Toeplitz matrix algorithm according to the bound
[1] N. D. Truong et al. "Machine Learning Cryptanalysis of a Quantum Random Number Generator," in IEEE Transactions on Information Forensics and Security, vol. 14, no. 2, pp. 403-414, Feb. 2019.
[1]

## Slide 10
Features:
  Real-time
  Active Quadrature switching
  Self-testing, self-calibrating, self-sustaining
  Non-classical source: squeezed state of light

## Slide 11: Squeezed State
Quadrature squeezed below shot-noise limit
Applications
  Quantum metrology, such as gravitational wave sensing [1, 2]
  Generation of entangled EPR state for quantum communication
  Quantum Information Processing
[1] Acernese, F., et al. "Increasing the astrophysical reach of the advanced Virgo detector via the application of squeezed vacuum states of light." Physical Review Letters 123.23 (2019): 231108.; [2] Tse, M., et al. "Quantum-enhanced advanced LIGO detectors in the era of gravitational-wave astronomy." Physical Review Letters 123.23 (2019): 231107.

## Slide 14: Results
Untrusted randomness
Trusted randomness

## Slide 17: Finite size effects

## Slide 18: Relaxing the I.I.D assumption
I.I.D assumption necessary for estimation of from the measured samples
→ The quantum state does not change between measurements
It can be relaxed by using smooth entropies, and a smooth version of the EUR [1, 2]:
[1] Tomamichel, et al. (2011). Uncertainty relation for smooth entropies. Physical review letters, 106(11), 110506.
[2] Coles et al. (2017). Entropic uncertainty relations and their applications. Reviews of Modern Physics, 89(1), 015002.

## Slide 19: Relaxing the bounded state assumption
Finite measurement range R
→ Energy bound assumption is necessary → Rounds with extremal values, if any, are discarded
There are modified versions of the EUR to circumvent the measurement range problem [1]
The modified EUR converges to the original EUR when R is large compared to spread of the source
[1] Bourassa et al. (2019). Entropic uncertainty relations and the measurement range problem, with consequences for high-dimensional quantum key distribution. JOSA B, 36(3), B65-B76.

## Slide 20: Conclusion & Outlook
We demonstrated a real-time, self-testing QRNG based on non-classical light.
We tested the QRNG with different sources and demonstrated the advantage of using squeezed light.
Speed limitation can be overcome with:
  Dedicated hardware for hashing
  Broadband squeezing
  Optical beam switching
Device can be miniaturized with on-chip squeezer and homodyne detection.

## Slide 21: Thank you for your attention!
Real-Time Source-Independent Quantum Random-Number Generator with Squeezed States Thibault Michel, J.Y. Haw, D. G. Marangon, O. Thearle, G. Vallone, P. Villoresi , P. K. Lam, S.M. Assad PhysRevApplied.12.034017
thibault.michel@anu.edu.au

## Slide 23: Details of experimental parameters
Protocol
  Digitization: number of bins: bins
  bin size (typical in SNU):
  Acquisition: Mixing down at 15 MHz with a 2MHz LPF
  200 KHz sampling frequency
  sample size:
  Hashing: Toepliz matrix algorithm
  Security parameter
Squeezed state production:
  Laser: ND:YAG, 1064/532nm, SN limited above 2 MHz
  Cavity: Doubly resonant, PPKTP crystal, 32 MHz linewidth, Finesse of 32
  Locking: cavity length: PDH with 30.3125 MHz phase modulation on the pump
  pump/seed phase + P-lock with 20.625 MHz phase modulation on seed
  Q-lock 11.875 MHz amplitude modulation on seed